## Slide 1
TRITONFLOW
Schema-Driven Multi-ISA AI Accelerator Compiler
Triton IR → declarative YAML ISA → bit-accurate execution on any custom accelerator Zero LLVM required · Zero C++ backend rewrites · Powered by torch.compile
torch.compile(model, backend="tritonflow")
182
Tests Passing
0.000e+00
Max GPU Error
18.6×
Compute Speedup
4 ops
vecadd Emitted
IICT CompilerTech Hackathon 2026 · Team segfault

## Slide 2
🛑 The Problem
Hardware innovation is outpacing software ecosystems.
When a startup or researcher designs a new AI accelerator (ASIC / FPGA / RISC-V GPGPU), integrating it into the PyTorch ecosystem today requires:
① Write a custom PyTorch C++ Device Extension from scratch (weeks)
② Fork the Triton compiler and modify MLIR lowering passes (months)
③ Build a custom LLVM backend and codegen pipeline (months)
④ Write a hardware runtime / driver layer (weeks)
⚠ This software moat takes 6–12 months and kills hardware innovation at the root.
Open accelerators like Vortex RVGPU have exceptional hardware — but zero PyTorch integration. TritonFlow closes that gap in 2 weeks.

## Slide 3
💡 The Solution: Declarative ISA Compilation
TritonFlow generates a complete, production-grade PyTorch backend from a simple declarative YAML description of your hardware's Instruction Set Architecture. You describe what your chip can do — TritonFlow handles parsing, recognition, instruction selection, emulation, and parity verification automatically.
# vortex_rvgpu.yaml — real open RISC-V GPGPU in YAML
name: vortex_rvgpu
instructions:
- name: TCU_WGMMA_SP32 kind: mac
tile: [32, 32] sparsity: 2:4
cost: 0.15 * m * n * k / (32*32) # 18.6x vs dense
constraints:
- all_of(m % 32 == 0, n % 32 == 0)
- name: DXA_COPY_2D kind: memory
cost: 0.15 * words # TMA-style async bulk DMA
constraints:
- all_of(stride[1] == 1, in_bounds_all())
- name: VADD kind: elementwise
cost: 0.05 * words # 32-lane SIMT vector ALU
✔ Real torch.compile backend — no API changes
✔ Triton IR parsed without LLVM build
✔ Fail-closed: 0.0% silent miscompilations
✔ Bit-accurate C++ + NumPy dual emulator
✔ Swap YAML → instant retarget + cost diff
✔ 182 passing tests, 3 live ISA targets
✔ Works on real open hardware (Vortex RVGPU)

## Slide 4
🏗️ How TritonFlow Works — End-to-End Pipeline
PyTorch torch.compile(…)
Track A Parser (TTIR → SSA)
Track C Recognition (Pointers & Loops)
Track B Selector (ISA Matching)
Track D Emulator (C++ / NumPy)
ISA YAML Schema (Declarative Config)
Intercepts torch.compile
Parses TTIR into SSA graph
Affine descriptor recovery + elision
Greedy min-cost instruction select
Bit-accurate execution + parity
Key invariant: every stage is independently testable — 182 tests verify contracts end-to-end.

## Slide 5
⚙️ Demo 1: PyTorch → Triton JIT → MLIR
1. PyTorch Frontend
# User writes standard PyTorch — zero API changes
@torch.compile(backend='tritonflow')
def matmul(x, y):
return torch.matmul(x, y) # (128×64) @ (64×128) → (128×128)
output = matmul(a, b) # TritonFlow intercepts here
2. Triton JIT Kernel
# Auto-lowered Triton JIT kernel
@triton.jit
def matmul_kernel(a_ptr, b_ptr, c_ptr,
M, N, K, stride_am, ...,
BM: tl.constexpr = 64,
BN: tl.constexpr = 64,
BK: tl.constexpr = 32):
for k in range(0, K, BK):
a = tl.load(a_ptrs) # [64×32] tile
b = tl.load(b_ptrs) # [32×64] tile
acc = tl.dot(a, b, acc) # MMA
tl.store(c_ptrs, acc)
3. Extracted MLIR (TTIR) — TritonFlow takes over here
// Extracted MLIR Triton Dialect (TTIR) — 63 SSA ops
module {
tt.func @matmul_kernel(%a_ptr: !tt.ptr<f32>, ...) {
%acc_25:3 = scf.for %_k = %c0 to %K step %c1
iter_args(%a_ptrs_34 = %a_ptrs, ...) {
%a = tt.load %a_ptrs_34 : tensor<64x32x!tt.ptr<f32>>
%b = tt.load %b_ptrs_35 : tensor<32x64x!tt.ptr<f32>>
%acc_37 = tt.dot %a, %b, %acc_36
: tensor<64x32xf32> * tensor<32x64xf32>
-> tensor<64x64xf32>
scf.yield %a_ptrs_40, %b_ptrs_43, %acc_37
}
}
}

## Slide 6
✂️ Address Math Elision: 18 TTIR Ops → 4 Hardware Instructions
For t0_vecadd (1024 elements): the descriptor engine absorbs 14 pointer-arithmetic ops into hardware DMA descriptors. Only 4 semantic instructions are emitted.
Before (TTIR — 18 ops):
# TTIR — 18 SSA operations
%c1024_i32 = arith.constant 1024 ; EPI → ELIDED
%pid = tt.get_program_id ; EPI → ELIDED
%offs = arith.muli %pid, %c1024 ; EPI → ELIDED
%offs_0 = tt.make_range 0:1024 ; EPI → ELIDED
%offs_1 = tt.splat %offs ; EPI → ELIDED
%offs_2 = arith.addi %offs_0, %offs_1 ; EPI → ELIDED
%x_4 = tt.addptr %x_ptr, %offs_2 ; EPI → ELIDED
... (8 more addr-math ops) ; EPI → ELIDED
%x_5 = tt.load %x_4 ; ← KEEP
%y_7 = tt.load %y_6 ; ← KEEP
%2 = arith.addf %x_5, %y_7 ; ← KEEP
tt.store %out_10, %2 ; ← KEEP
After (Hardware ISA — 4 ops):
# Emitted hardware program — 4 ops
[00] DMA1D src=global:%x_ptr
tile=[1024] stride=[1]
offset=[1024*%pid]
cost=1024.0 cycles
[01] DMA1D src=global:%y_ptr
tile=[1024] stride=[1]
offset=[1024*%pid]
cost=1024.0 cycles
[02] EPI op=add in0=%x_5 in1=%y_7
cost=512.0 cycles
[03] DMA1D dst=global:%out_ptr value=%2
cost=1024.0 cycles
Coalescing: 100.0% (128B req = 128B transacted, 4 transactions) · Bank conflicts: 0

## Slide 7
🔍 Semantic Recovery: α / β Attribute Splitting
Before choosing any hardware instruction, TritonFlow analyses TTIR to recover loop induction variables, build SSA def-use chains, and extract hardware-agnostic affine access descriptors (α = computation attributes, β = addressing attributes).
SSA Value | Source Op | Idiom | Recovered Semantic Descriptor
%_k | scf.for | control_flow | loop induction: 0 → K, step 32 ¦ iter_args: %a_ptrs, %b_ptrs, %acc
%a | tt.load | memory | base=%a_ptr, sizes=[64,32], strides=[stride_am, stride_ak], offset=[64*%pid_m*stride_am, 0]
%b | tt.load | memory | base=%b_ptr, sizes=[32,64], strides=[stride_bk, stride_bn], offset=[64*%pid_n*stride_bn, 0]
%acc_37 | tt.dot | mac | tile=(64, 64, 32), precision=tf32, acc_dtype=f32, order=k_major_sequential
%a_ptrs_38 | arith.muli | elementwise → SUBSUMED | stride advance: stride_ak × 32 → folded into DMA descriptor
%a_ptrs_40 | tt.addptr | elementwise → SUBSUMED | pointer increment: %a_ptrs_34 + %splat_39 → folded into DMA descriptor
(store) | tt.store | memory | base=%c_ptr, sizes=[64,64], strides=[stride_cm, stride_cn], offset=[64*pid_m*scm + 64*pid_n*scn, 0]

## Slide 8
⚡ Lowering Diff: Abstract TTIR → Vortex RVGPU Hardware
Abstract TTIR ops → concrete hardware instructions (matmul inner loop)
--- Pre-ISA Abstract TTIR
+++ Target: VORTEX_RVGPU (RISC-V SIMT GPGPU)
@@ Inner Compute Loop Lowering @@
- %a = tt.load %a_ptrs_34 : tensor<64x32x!tt.ptr<f32>>
+ LDG src=global:%a_ptr[tile=[64,32], strides=[stride_am,stride_ak]] ; cost=1024.0
- %b = tt.load %b_ptrs_35 : tensor<32x64x!tt.ptr<f32>>
+ LDG src=global:%b_ptr[tile=[32,64], strides=[stride_bk,stride_bn]] ; cost=1024.0
- %acc_37 = tt.dot %a, %b, %acc_36
- : tensor<64x32xf32> * tensor<32x64xf32> -> tensor<64x64xf32>
+ TCU_WGMMA_SP32 a=%a b=%b acc=%acc ; cost=19.2 (2:4 structured sparsity, 2.0×)
- %a_ptrs_38 = arith.muli %sak, %c32_i32
+ VMUL dst=%a_ptrs_38, src0=%sak, src1=%c32 ; cost=0.1 (SIMT vector multiplier)
- %a_ptrs_40 = tt.addptr %a_ptrs_34, %splat_39
+ VADD dst=%a_ptrs_40, src0=%a_ptrs_34, src1=%splat ; cost=102.4 (32-lane vector ALU)
TRITONFLOW1 vs VORTEX_RVGPU — instruction delta
TTIR Op | TRITONFLOW1 | VORTEX_RVGPU | Speedup
tt.load (×2) | DMA1D (cost=2048.0) | LDG (cost=1024.0) | −50% ✔
tt.dot | MAC16 (cost=358.4) | TCU_WGMMA_SP32 (19.2) | −18.6× ✔
arith.muli | EPI (cost=0.5) | VMUL (cost=0.1) | −5× ✔
tt.addptr | EPI (cost=1024.0) | VADD (cost=102.4) | −10× ✔

## Slide 9
📊 Demo 2: 3-Way Architectural Comparison (Live)
Same TTIR kernel, same Python code — three radically different hardware targets, zero compiler C++ rewritten.
Dimension | TRITONFLOW1 (Systolic ASIC) | TRITONFLOW2 (Banked ASIC) | VORTEX_RVGPU (RISC-V GPGPU)
Hardware Target | Flat Systolic Accelerator | Multi-bank Domain ASIC | RISC-V SIMT GPGPU (open HW)
Primary Compute | MAC16 — 16×16 systolic array | OPU32 — 32×32 outer product | TCU_WGMMA_SP32 — sparse WG-MMA
Memory Engine | DMA1D / DMA2D (flat) | LDS2D (16-bank interleaved) | DXA async bulk DMA (1D–5D)
Sparsity Support | Dense only (1.0×) | Dense only (1.0×) | 2:4 Structured Sparsity (2.0×)
Micro-arch Gate | Static FIFO Pipeline | Bank Conflict Arbiter | Warpgroup Lockstep Gate
Compute Cost / tile | 358.4 cycles (MAC16) | 70.4 cycles (OPU32) | ★ 19.2 cycles (18.6× faster!)
Total Kernel Cost | 35,773 cycles | 28,402 cycles (−20.6%) | ★ 6,838 cycles (5.2× speedup)
YAML Lines to Target | < 80 lines | < 100 lines | < 200 lines (full TCU + DXA)
★ Swap one YAML file → compiler instantly re-targets and reports the full cost delta. A second ISA is the only falsifiable test of declarative compilation.

## Slide 10
🔬 Demo 3: Cost-Driven Instruction Selection Audit
For every operation the compiler evaluates ALL schema candidates against fail-closed constraint predicates, models execution cost exactly, and greedily selects the cheapest admissible candidate. Every decision is deterministic and fully logged.
Candidate | Constraint Predicate | Verdict | Modeled Cost | Compiler Decision
TCU_WMMA16 | all_of(m % 16 == 0, n % 16 == 0) | ✔ PASS | 204.8 MACs | Rejected (higher cost)
TCU_WGMMA32 | all_of(m % 32 == 0, n % 32 == 0) | ✔ PASS | 32.0 MACs | Rejected (higher cost)
TCU_WGMMA_SP32 | all_of(m % 32 == 0, 2:4 sparsity) | ✔ PASS | 19.2 MACs | ★ SELECTED (lowest cost)
TCU_WGMMA_MXFP8 | all_of(m % 32 == 0, block_scale == 32) | ✔ PASS | 25.6 MACs | Rejected (higher cost)
TCU_MMA32 | all_of(m % 32 == 0, n % 32 == 0) | ✔ PASS | 32.0 MACs | Rejected (higher cost)
FEDP_DOTPROD | lane_width == 32 | ✖ FAIL | — | Rejected (inadmissible)
✔ TCU_WGMMA_SP32 selected — satisfies all tile predicates, lowest valid cost (19.2 vs 32.0 MACs). 2:4 structured sparsity gives 2.0× effective throughput.
# Every selection decision is deterministic, auditable, and logged
# vortex_rvgpu | tt.dot | tile=(64, 64, 32)
Candidate TCU_WMMA16 admissible=True cost=204.8 rejected
Candidate TCU_WGMMA32 admissible=True cost= 32.0 rejected
Candidate TCU_WGMMA_SP32 admissible=True cost= 19.2 ★ SELECTED
Candidate TCU_WGMMA_MXFP8 admissible=True cost= 25.6 rejected
Candidate FEDP_DOTPROD admissible=False rejected

## Slide 11
🛑 Demo 5: Fail-Closed Integrity — Honest Refusal on t3_modulo
Input: Non-Affine Kernel
# t3_modulo — unstructured pointer arithmetic
@triton.jit
def modulo_kernel(x_ptr, out_ptr, N, ...)
pid = tl.program_id(0)
offs = (pid * BL + tl.arange(0, BL)) % N
# ↑ non-affine modulo wrap!
x = tl.load(x_ptr + offs) # irregular
tl.store(out_ptr + offs, x)
Compiler Output: Fail-Closed
# TritonFlow compiler output — honest refusal
UNSUPPORTED op=arith.remsi at %x_ptr
reason: unstructured access — modulo pointer
arithmetic cannot be described by an
affine stride/offset decomposition.
UNSUPPORTED op=tt.load at %x_4
reason: pointer operand unavailable
→ Compiler triggers PyTorch eager fallback
→ Zero silent miscompilations
→ Complies with contract FR-025
0.0%
Silent Miscompilation Risk
2
UNSUPPORTED markers emitted
FR-025
Contract specification satisfied
100%
Negative control test pass rate

## Slide 12
✅ Results & Verification
182 / 182
Contract & Unit Tests Passing (100% pass rate, 17.45 s run)
0.000e+00
Max Abs Error vs NVIDIA GPU (Bit-accurate numerical parity)
18.6×
Compute speedup: Vortex vs TF1 (TCU_WGMMA_SP32 vs MAC16)
5.2×
Total kernel speedup (6,838 vs 35,773 cycles)
< 200 lines YAML
Full Vortex RVGPU backend (Zero LLVM / C++ required)
4 ops
vecadd emitted instructions (down from 18 — full elision)
Verified live on real NVIDIA GeForce GTX 1650 · 3 production ISA targets · 13 test files · pybind11 C++ fast path

## Slide 13
🎯 Strategic Positioning: What We Claim & What We Don't
What TritonFlow claims (and proves):
✔ Triton IR → declarative YAML ISA backend is technically feasible and ships today
✔ A second ISA (Vortex RVGPU) is the only falsifiable proof — we have three
✔ Bit-accurate numerical parity with real NVIDIA GPU (0.000e+00 max error)
✔ Fail-closed: unstructured kernels get honest UNSUPPORTED, not corrupt output
✔ torch.compile front-door integration — zero user API changes needed
What TritonFlow does NOT claim:
✖ CUDA hijack or interception of vendor CUDA kernels (closed libraries / ptxas)
✖ Autotune-for-cuBLAS performance — not the goal
✖ 'Beyond ACT' — ACT (OOPSLA 2026) pioneered declarative schemas for XLA-HLO;
TritonFlow extends that thesis to the modern torch.compile + Triton IR stack
"A second ISA is the only falsifiable test of declarative compilation." — TritonFlow thesis

## Slide 14
TritonFlow
Democratising AI Hardware Design
From YAML spec to a running torch.compile backend in minutes — not months.
🔗 github.com/Incharajayaram/segfault-tritonflow
⚡ PYTHONPATH=src python3 tritonflow_demo.py
🔬 PYTHONPATH=src python3 tools/demo_live.py
📊 PYTHONPATH=src python3 demo_diff.py
IICT CompilerTech Hackathon 2026 · Team segfault